## Slide 1: IRIS RECOGNITION SYSTEM
Rasha Tarawneh Omamah Thunibat
Presented to:
Dr Ahmad Alhassanat
Mutah university
Biometric course :
Notes: Lecture by Rasha Tarawneh, Omamah Thunibat and Dr. Ahmad B. A. Hassanat

## Slide 2: Overview:
Introduction
What the iris?
Why iris?
History of iris Recognition
Applications
Methods of iris recognition system
Image Acquisition
Segmentation
Normalization
Iris Feature Encoding
Iris code matching
Applications
Disadvantages
Conclusion
References

## Slide 3: Introduction
It is considered to be the most accurate biometric technology available today.
Iris recognition is a method of biometric identification and authentication that use pattern-recognition techniques based on high resolution images of the irises of an individual's eyes .

## Slide 4: What is Iris ?
The colored ring around the pupil of the eye is called the Iris

## Slide 5: What is Iris ?
The iris is a thin circular diaphragm, which lies between the cornea and the lens of the human eye.
The iris is perforated close to its centre by a circular aperture known as the pupil.
The function of the iris is to control the amount of light entering through the pupil.
The average diameter of the iris is 12 mm, and the pupil size can vary from 10% to 80% of the iris diameter [2].

## Slide 6: What is Iris ?
The iris consists of a number of layers, the lowest is the epithelium layer, which contains dense pigmentation cells. The stromal layer lies above the epithelium layer, and contains blood vessels, pigment cells and the two iris muscles.

## Slide 7: What is Iris ?
The density of stromal pigmentation determines the colour of the iris.
The externally visible surface of the multi-layered iris contains two zones, which often differ in colour An outer ciliary zone and an inner pupillary zone, and these two zones are divided by the collarette – which appears as a zigzag pattern[3].

## Slide 8: Why the Iris?
Externally visible highly protected internal organ.
Unique patterns.
Not genetically connected unlike eye color.
Stable with age.
Impossible to alter surgically.
Living Password, Can not be forgotten or copied.
Works on blind person.
User needs not to touch appliances.
Accurate , faster , and supports large data base.

## Slide 9: Why the Iris?

## Slide 10: Why the Iris?
Comparison between cost and accuracy

## Slide 11: History of Iris Recognition
1997-1999
1987
1987
1980
The concept of Iris Recognition was first proposed by Dr. Frank Burch in 1939.
It was first implemented in 1990 when Dr. John Daugman created the algorithms for it.
These algorithms employ methods of pattern recognition and some mathematical calculations for iris recognition.

## Slide 12: Applications
. ATMs
.Computer login: The iris as a living password.
· National Border Controls
· Driving licenses and other personal certificates.
· benefits authentication.
·birth certificates, tracking missing.
· Credit-card authentication.
· Anti-terrorism (e.g.:— suspect Screening at airports)
· Secure financial transaction (e-commerce, banking).
· Internet security, control of access to privileged information.

## Slide 13: Methods Of IRIS Recognition System
In identifying one’s iris, there are 2 methods for its recognition and are:
      Active
      Passive
The active Iris system requires that a user be anywhere from six to fourteen inches away from the camera.
The passive system allows the user to be anywhere from one to three feet away from the camera that locates the focus on the iris.

## Slide 14: Iris Recognition Diagram
Image Acquisition
Iris Segmentation
Normalization
Feature Encoding
Feature Matching
Iris Templates Database
Eye Image
Iris Region
Feature points in the iris region
Iris Template
Identify or Reject Subject

## Slide 15: Image Acquisition
The first step, image acquisition deals with capturing sequence of iris images from the subject using cameras and sensors with High resolution and good sharpness.
These images should clearly show the entire eye especially iris and pupil part, and then some preprocessing operation may be applied to enhance the quality of image e.g. histogram equalization, filtering noise removal etc.
(CASIA) eye image database

## Slide 16: Segmentation/concept
The first stage of iris segmentation to isolate the actual iris region in a digital eye image.
The iris region, can be approximated by two circles, one for the iris/sclera boundary and another, interior to the first, for the iris/pupil boundary.

## Slide 17: Segmentation/eyelids
the derivatives in the horizontal direction for detecting the eyelids, and in the vertical direction for detecting the outer circular boundary of the iris .
Taking only the vertical gradients for locating the iris boundary will reduce influence of the eyelids when performing circular Hough transform.

## Slide 18: Segmentation/Hugh
The circular Hough transform can be employed to deduce the radius and centre coordinates of the pupil and iris regions:
Firstly, an edge map is generated by calculating the first derivatives of intensity values in an eye image and then thresholding the result.
From the edge map, votes are cast in Hough space for the parameters of circles passing through each edge point, These parameters are the centre coordinates xc and yc, and the radius r, which are able to define any circle according to the equation :
A maximum point in the Hough space will correspond to the radius and centre coordinates of the circle best defined by the edge points.

## Slide 19: Segmentation/eyelash
eyelashes are treated as belonging to two types :
1 -separable eyelashes:
which are isolated in the image .
2-multiple eyelashes:
which are bunched together and overlap in the eye image.
Eyelids and Eyelashes are the main noise factor in the iris image.
These noise factors can affect the accuracy of the iris recognition system.
After applying circular Hough transform to iris, we are applying linear Hough transform and we get line detected noise region in the iris image.
We have to remove these detected eyelids and eyelashes from the iris image Thresolding is used for the removal of eyelashes. Then, the noise free iris image can be available for future use.

## Slide 20: Segmentation Diagram
1- Edge Detector
2- Hough Transform
Smoothing
Finding gradient
Double thresholding
Edge
LINEAR HOUGH TRANSFORM
CIRCULAR HOUGH TRANSFORM

## Slide 21: Segmentation( cont…)
Process of finding the iris in an image
  a. Iris and pupil localization: Pupil and Iris are considered as two circles using Circular Hough Transform .
b. Eye lid detection and Eye lash noise removal using linear Hough Transform method.

## Slide 22: Normalization
Various Normalisation methods :
1- Daugman’s Rubber sheet Model by Daugman [2]
2- Image Registration modlyed by Wildes et al .[9]
3- Virtual Circles by Boles [14] .

## Slide 23: Normalization
Once the iris segmented ,the next stage transform the iris region so that it has fixed dimensions in order to allow comparisons.
Since variations in the eye like pupil dilation and the inconsistence iris normalization is needed.
Pupil dilation inconsistence iris
Normalization process involves unwrapping the iris and converting it in to its polar equivalent .

## Slide 24: Normalization ( cont...)
It is done using Daugman’s Rubber sheet model .
The centre of the pupil was considered as the reference point, and radial vectors pass through the iris region .
A number of data points are selected along each radial line is defined as the radial resolution. The number of radial lines going around the iris region is defined as the angular resolution.

## Slide 25: Normalization ( cont...)

## Slide 26: Normalization ( cont...)
Normalisation produces a 2D array with horizontal dimensions of angular resolution and vertical dimensions of radial resolution.
Rubber sheet model does not compensate for rotational inconsistencies

## Slide 27: Feature Encoding
Various feature encoding methods :
1-Gabor Filters employed by Daugman in [2] and Tuama.[6]
2- Log-Gabor Filters employed by D. Field.[15]
.
3- Haar Wavelet employed by Lim et al.. [16]
4- Zero –crossing of the 1D wavelet employed by Boles and Boashash .[14]
5- Laplacian of gaussian filters employed by Wildes et al[9]

## Slide 28: Feature Encoding
Feature Encoding : creating a template containing only the most discriminating features of the iris .
Extracted the features of the normalized iris by filtering the normalized iris region . [6]
a Gabor filter is a sine ( or cosine) wave modulated by a Gaussian . it is applied on the entire image at once and unique features are extracted from the image
Feature encoding was implemented by convolving the normalized iris with 1D Gabor wavelets.

## Slide 29: Feature Encoding ( cont …)

## Slide 30: Feature Encoding ( cont …)
Daugman demodulates the output of the Gabor filters in order to compress the data this is done by quantising the phase information in to four levels , for each possible quadrant in the complex plane . [7]
The demodulation and phase Quantisation process can be represented as
where h{Re, Im} can be regarded as a complex valued bit whose real and imaginary components are dependent on the sign of the 2D integral, and I( ρ,θ ) is the raw iris image in a dimensionless polar coordinate system.

## Slide 31: Feature Encoding ( cont …)
Using real and imaginary values, the phase information is extracted and encoded in a binary pattern .
The total number of bits in the template will be the angular resolution times the radial resolution , times 2, times number of filters used .
The number of filters,their centre frequencies and parameters of the modulating Gaussian function must be detecting according to the used data base .

## Slide 32: Feature encoding process

## Slide 33: Feature Matching
Various feature matching methods :
1- Hamming distance employed by Daugman [2]
2- Weighted Euclidean Distance employed by Zhu et al[17] .
3- Normalised correlation employed by Wildes [9] .

## Slide 34: Feature Matching
The Hamming Distance was chosen as a matching metric , which gave a measure of how many bits disagreed between two templates .
When the hamming distance of two templates is calculated , one template is shifted left and right bit-wise and a number of hamming distance values are calculated from successive shifts , in order to account for rotational inconsistencies .

## Slide 35: Feature Matching ( cont …)
The actual number of shifts required to normalise rotational inconsistencies will be determined by the maximum angle difference between two images of the same eye .
One shift is defined as one shift to the left , followed by one shift to the right .
This method is suggested by Daugman . [7]

## Slide 36: Feature Matching ( cont …)

## Slide 37: Research’s Database
The Chines Academy of Sciences – Institute of Automation (CASIA) eye image database contains 756 greyscale eye images with 108 unique eyes or class are taken from two sessions .[8]

## Slide 38: FAR & FRR for the ‘CASIA-a’ data set
Threshold | FAR (%) | FRR (%)
0.20 | 0.000 | 99.047
0.25 | 0.000 | 82.787
0.30 | 0.000 | 37.880
0.35 | 0.000 | 5.181
0.40 | 0.005 | 0.238
0.45 | 7.599 | 0.000
0.50 | 99.499 | 0.000
Table 1 – False accept and false reject rates for the ‘CASIA-a’ data set with different separation points using the optimum parameters.

## Slide 39: Disadvantages
Accuracy changes with user’s height ,illumination , Image quality etc.
Person needs to be still, difficult to scan if not co-operated.
Risk of fake Iris lenses.
Alcohol consumption causes deformation in Iris pattern
Expensive .

## Slide 40: Conclusion
Highly accurate but easy
Fast
Needs some developments
Experiments are going on
Will become day to day technology very soon

## Slide 41: References
[1] · http://www.cl.cam.ac.uk
[2] J. Daugman. How iris recognition works. Proceedings of 2002 International Conference on Image Processing, Vol. 1, 2002.
[3]E. Wolff. Anatomy of the Eye and Orbit. 7th edition. H. K. Lewis & Co. LTD, 1976.
[4] L.Flom and A. Safir : Iris Recognition System .U.S. atent No.4641394(1987).
[5] T. Chuan Chen K . Liang Chung : An Efficient Randomized Algorithm for Detecting Circles.
Computer vision and Image Understanding Vol.83(2001) 172-191.
[6] Amel saeed Tuama “ It is Image Segmentation and Recognition Technology” vol-3 No.2 April 2012 .
[7] S. Sanderson, J. Erbetta. Authentication for secure environments based on iris scanning technology. IEE Colloquium on Visual Biometrics, 2000 .
Notes: http://www.cl.cam.ac.uk

## Slide 42: References
[8] E. Wolff. Anatomy of the Eye and Orbit. 7th edition. H. K. Lewis & Co. LTD, 1976 .
[9] R. Wildes, J. Asmuth, G. Green, S. Hsu, R. Kolczynski, J. Matey, S. McBride. A system for automated iris recognition. Proceedings IEEE Workshop on Applications of Computer Vision, Sarasota, FL, pp. 121-128, 1994.
[10] W. Kong, D. Zhang. Accurate iris segmentation based on novel reflection and eyelash detection model. Proceedings of 2001 International Symposium on Intelligent Multimedia, Video and Speech Processing, Hong Kong, 2001.
[11] C. Tisse, L. Martin, L. Torres, M. Robert. Person identification technique using human iris recognition. International Conference on Vision Interface, Canada, 2002.
[12] L. Ma, Y. Wang, T. Tan. Iris recognition using circular symmetric filters. National Laboratory of Pattern Recognition, Institute of Automation, Chinese Academy of Sciences, 2002.
[13] N. Ritter. Location of the pupil-iris border in slit-lamp images of the cornea. Proceedings of the International Conference on Image Analysis and Processing, 1999.

## Slide 43: References
[14] W. Boles, B. Boashash. A human identification technique using images of the iris and wavelet transform. IEEE Transactions on Signal Processing, Vol. 46, No. 4, 1998.
[15] D. Field. Relations between the statistics of natural images and the response properties of cortical cells. Journal of the Optical Society of America, 1987.
[16] S. Lim, K. Lee, O. Byeon, T. Kim. Efficient iris recognition through improvement of feature vector and classifier. ETRI Journal, Vol. 23, No. 2, Korea, 2001.
[17] Y. Zhu, T. Tan, Y. Wang. Biometric personal identification based on iris patterns. Proceedings of the 15th International Conference on Pattern Recognition, Spain, Vol. 2, 2000.